## Slide 1
Introduction to Communication Engineering(01CT0303)
Conceptualization
Image frequency and how RF Bandwidth reject image frequency
Prepared by:
Mandeep Dangar
91900133017
B.Tech(SEM-3)
Guided by:
Prof. Chandrasinh Parmar
Head of department(ICT)

## Slide 2: What is image frequency?
The image frequency is an undesired input frequency which is demodulated by super heterodyne receivers along with the desired incoming signal. This results in two stations being received at the same time, thus producing interference.

## Slide 3: Block diagram of superheterodyne receiver
RF AMPLIFIER
MIXER
LOCAL OSCILLATOR
IF
AMPLIFIER
DETECTOR
POWER/
AUDIO
AMPLIFIER
ANTENNA

## Slide 4: Image frequency
To understand concept of Image frequency we need to remove RF amplifier and then analyze the process of demodulating of super heterodyne receiver.
By removing RF amplifier our antenna received signal will be processed by mixer and all the frequency of AM (550KHz to 1720 KHz) will be available at mixer.
Now, we will understand concept of image frequency by one example.

## Slide 5: Image frequency example
Suppose we want to listen 600 KHz frequency (fs)of AM band.
In this case we are supposing our IF frequency of 450 KHz.
Local oscillator frequency(fo).
Our mixer output will give us fo, fs, f0-fs, fo+fs .
IF will allows f0-fs which have value of 450 KHz to pass through it.
So, to hear 600 KHz we need to tune local oscillator to 1050KHz.

## Slide 6
MIXER
LOCAL OSCILLATOR
IF
AMPLIFIER
DETECTOR
POWER/
AUDIO
AMPLIFIER
550 1750
Frequency available at mixer input
Local oscillator frequency (1050 KHz)
Explanation of image frequency for 600 KHz
fs
At the end of mixer we will get,
fo=1050Khz
Fs=600KHz
fo-fs=450KHz
fo+fs=1500KHz
But we have also 1500 KHz at input of mixer and it will give output of mixer for
fs-fo=450KHz
And this will gives us undesired output which we don’t want to listen
And this undesired frequency of 1500 KHz is called Image frequency for 600 KHz.
And equation for Image frequency is = desired frequency + 2*(IF)

## Slide 7: Need of RF amplifier
RF amplifier helps us to overcome Image frequency.
For that RF bandwidth should be <2*(IF)
Because we will get image frequency when our bandwidth allows frequencies which are twice of IF amplifier.
Hence RF bandwidth will not allow image frequency in input and we will get desired output.

## Slide 8
Thank you